Colour probe for the visually handicapped persons

Fumiya Furuno

A battery-powered pocketable colour probe is now under developmentwhich
discriminates the colour of an object and using a voice output tells the
persons its colour. Thirteen kinds of colours can be discriminated so far.
These are white, grey, black, red, pink, brown, orange, yellow, green,
blue, light-blue, dark-blue, and purple. This probe is also given a
function of a light probe. Its size, at present, is about 13.8 x q,q x 2.g
cm ' and it weighs about 150 g. It will serve the visually handicapped
persons in their daily life, vocational life and in education. The
developement is now proceeding towards higher accuracy and increasing the
number of colours discriminated.

1. Introduction

The visually handicapped persons can acquire much information of an object
near them by touching it mainly by their fingers and hands. For example,
they can recognize its shape, its material, its temperature, its weight,
its size and roughness of its surface. They, however, can never recognize
the colour of an object at all.We are now developing a small apparatus for
discriminating colour of an object and telling the persons the name of the
colour. The last year,a prototype of the colour probe was presented at the
conference(I) and on the journa1(2).In this workshop an improved colour
probe is presented which has been miniaturized and to which new functions
such as light sensing function have been added.The result of test and
evaluation and that of hearing from the disabled persons who trially used
this probe are also presented.

2. Principle to recognize colours

The colour of an object is determined by both the spectral distribution of
the light thrown onto the object and the spectral reflectance of its
surface. A small lamp placed in the pointed head of this probe radiates the
light on an object and the spectral distribution of the direct light from
the lamp and that of the reflected light from the object are measured. In
order to measure the distribution and the reflectance stated above, six
light sensors are used in this probe.The colour can be calculated out by
putting the output from the six sensors into some formulae experimentally
derived.

3. Principle of the light probe

One of the six sensors in this probe which has the same spectral luminus
efficiency as the normal human eye is used to detect the intensity of the
visual light. The output of this sensor is converted to a frequency of
sound proportional to the intensity of the input light.

4. System configuration

The lamp controlled by the microcomputer illuminates an object and the
direct light from the lamp is received by the three pieces of light sensors
and the reflected light from the object is received by other three light
sensors. The output of these six sensors are amplified,multiplexed,and
converted to digital values and introduced to the microcomputer, which
calculates X, Y and Z called tristimulus values and then x, y called
chromaticity coordinates. AII colours are specified by the above x, y and Y
values. The microcomputer decides the colour from these x,y and Y values
and then selects the word in the ROM corresponding to the decided
colour.The selected word is then picked up and converted to analog
value,amplified and spoken out from the speaker or the earphone. On the use
as the light probe,the lamp is left off and only one sensor's output is
amplified, converted to digital value and introduced to the microcomputer.
The frequency of sound proportional to the intensity of the input light is
produced by the microcomputer and is converted to analog value and then put
out from the speaker or the earphone.

5. Structure and operation

This probe is so designed that it can be carried in a pocket or a handbag
and that it can be operated by one hand.Its size is 13.8x4.4x2.8 cm3 and it
weighs abot 150 g. Fig.l shows the dimensions and the structure. An 8 bit
microcomputer plays an indispensable role to have made this probe small
sized.
When a person wants to know the colour of some object, all he or she has to
do is to put on the power switch,to throw the mode switch to the colour
mode, to put the tip of the probe on the object and to push the push
switch. Then, the voice representing the colour can beheard from the
speaker or the earphone.If the push switch is kept on pushed,the voice can
be heard once each 3 seconds successively.
On the light probe use, a person hasonly to put on the power switch and
tothrow the mode switch to the light mode,then he can hear the note
correspondingto the illuminance at the tip of theprobe. The brighter the
light, thehigher the tone.
Two alkaline dry batteries(size AA)areused to operate this probe. This can
beused continuously about 8 hours as a colour probe and about 12 hours as a
lightprobe without renewing the batteries. If the batteries' voltage down
to belowthe usable level,the voice "renew the batteries"can be heard from
the probe.

6. The test result

In order to ascertain the accuracy of this colour probe,about 300 samples
weremeasured. These are papers, clothes, plastics, leathers, furnitures,
foods,drinks, flowers, leaves and so on. The result shows that although the
accuracyreached to about 95% on the objects with higher chromaticity and
higher lightness, it reduced to a lower figure on the objects with lower
chromaticity andlower lightness.Liquids showed lower accuracy than solids
did.The directivity as a light probe was measured.It has a relatively sharp
directivity of ñ13 degrees. This means that input light intensity into this
probedecreases to a half value if its pointing direction is deflected 13
degree fromthe initially pointed light source.

7. Evaluation by trial use

This probe is now being used by the visually handicapped persons in order
to beevaluated. According to some users, it will be usefull for
coordinating theclothes being put on in their daily life, for example, a
blouse and skirt, ashirt and trousers, socks and shoes, a shirt and necktie
etc.. Other personsmentioned that after washing many pairs of socks at a
time,it served to findout which two are a pair.It will also be used
effectively at the school for theblind when a teacher gives a lesson in
arts and the blind pupils observe notonly the objects in lesson, but also
everything around them such as flowers,leaves and trees in the garden. In
the office, for example, it can be used tofind a specific file among the
many different coloured files. The light probecan tell the blind persons
the direction of the lamp and if it is on or off.

8. Conclusions

A pocketable colour probe has been realized which discriminates
thirteendifferent colours and tells the operator the name of the colour.
It, moreover,tells him or her the intensity of the light by the tone of
sound.From the viewpoint of accuracy, much effort will have to be made
hereafter.Itwill also be necessary to discriminate dark,vague and
intermidiate colours.

9. Acknowledgment

The auther wishes to thank the many visually handicappedpersons and their
instructors who gave him valuable proposals and informations.He also thanks
to J. Miyajima, k. Muroga and T. Kudo for designing and constructing this
probe.

10. References

(l) F. Furuno : Colour Discriminating Apparatus for the Blind,
IstInternationalConference on Computers for Handicapped Persons, Wien,134-
143,1989
(2) F. Furuno : Colour discriminating apparatus for the blind, Journalof
Microcomputer Applications, 13, 155-164, 1990