Software applications in the communication between a computer and its blind
user as well as in the modernization of braille production based on the
latest developments in Poland

Helena Jakubowska, Stanislaw Jakubowski

A computer cannot be considered as a suitable and sufficient aid for a
blind person, unless the user is provided with an efficient system of
communication with this sophisticated tool. To achieve this goal it is
necessary to comply with the following terms:
1. The blind user should be capable of entering all possible data.
2. The widest possible range of data displayed on the screen should be
accessible to the user.
One of the ways to solve the problem mentioned in item 1. consists in
making a program by which selected keys of the standard computer keyboard
take the function of the brailler keyboard. A short description of such a
program has been given.
The second condition i.e. making the information from the screen accessible
to the blind user can be fulfilled by the following means :
- Synthetic speech.
- Magnified characters on the screen.
- Optacon.
- Braille display.
In Poland the first two techniques are more applicable due to their lower
cost. The most important features of programs serving the above purposes
have been discussed in this paper.
Another significant field of application of computer techniques is braille
production. The most important functions of a software package worked out
for this domain have been described. The paper ends up with a short
presentation of methods of publishing large print periodicals. This report
summarizes all significant results achieved in the field of computerized
braille and large print production by various Polish authors since
Winterthur conference in 1986.

Since the previous conference in Winterthur during which I was presenting
some investigations on computerized braille production started in Poland I
have not been able to demonstrate any applications of this work so far.
Therefore, it is a great pleasure for me to take this opportunity to report
that the Printing House of the Polish Association of the Blind has been
successful in employinga computer techniques in the production of braille
and large print periodicals and books In addition, pioneer home-production
devices and programs designed to facilitate the blind or partially sighted
user's communication with a computer, have been introduced.
Considering the growing applicability of computers in the work of and for
the blind one can notice that in many countries computerization was
originally introduced in braille printing houses and only after several
years gradually reached individuals. It was long before first blind users
could utilize their own computers at home that the total blind community
were provided with books and magazines prepared with the use of computer
techniques and modern braille printers. In Poland the situation is similar,
although we cannot clearly distinguish between the two following stages,
since before it was possible to computerize our printing house, a team of
programmers managed to prepare first packages making a computer available
to the user with impaired vision.
For many blind users it becomes rather difficult to get well- acquainted
with the complicated computer keyboard. Some, however, are quite efficient
in using a brailler and it is for them that a resident program called
Keybrl was written by one of our blind programmers, I. Buslowicz, making it
possible to enter data in the six- or eight-dot braille notation. There are
several characteristics distinguishing this program among a group of others
of the same type. A blind person may alternately use the standard computer
keyboard or a set of selected keys taking the functions of brailler keys
and thus corresponding to particular dots. To switch over to either of the
two keyboard functions you simply press an alt-space keystroke. In the six-
dot notation the number and capital signs can be used without any
limitations. The pressing of either of these dot combinations does not make
any additional symbols appear on the screen and their conversion into the
standard system takes place automatically. Thus, for instance, if the
letter "a" is preceded by the number sign, the number 1 will be displayed
on the screen. If, however, we put the capital sign in front of the letter
"a", we will see it on the screen as "A". The use of "r" parameter while
calling Keybrl program provides the user with a possibility to write with
the right hand only. The parameter "l" has been designed to switch over to
the left hand braille keyboard. A modified version of keybrl program has
successfully been applied as a keyboard driver to the German production
Blindenstudienanstalt printing machine and due to this improvement blind
copyists who used to work with printing machines of this type can retain
their previous manner of writing while using electronic braille devices.
Another necessary condition for the user with impaired vision to be able to
work with a computer is that he or she should be able to perceive all the
information displayed on the screen. In Poland, where computers have been
accessible to blind individuals since not long ago, software techniques are
obviously preferable in solving this problem. Thus, for example, Lens
program designed to magnify characters on the screen does not require any
hardware additions or modifications. Lens, prepared also by I. Buslowicz,
is capable of magnifying a fragment of text consisting of 5 or 6 lines, 10
characters each. The user can choose among three magnification ranges: 3x,
5x and 10x. One of the serious limitations of the program, however,
consists in the fact that it is suitable for the text mode only.
Similarly to the talking book being the most popular traditional form of
access to literature, a speech synthesizer is becoming the most preferable
computer aid among the blind in Poland. Two models of the device are
available: one applicable to IBM PC and the other adapted to ZX Spectrum
class computers. The synthesizer is connected to the Centronics output and
employs the central processor of a computer. A so called sampling synthesis
has been used here. Polish phonemes have been stored on a floppy disk as a
file. With the use of the synthesizer we can not only obtain all the
information from the screen but also get an acoustic representation of
every key stroke. This synthesizer is suitable for the most popular text
editors such as WordPerfect, WordStar or Word. The synthesizer, including
software, costs less than 200 dollars. Phonemes have been electronically
recorded in a digital form by Jan Grebecki, a skilful technician, while the
synthesis and software necessary for the user have been made by one of our
blind programmers, Marek Kalbarczyk.
The modernization of our printing house was undertaken in 1988. Braille
printers: Puma-V and Braillo 400 have been imported to publish braille
periodicals and books. All the necessary software has been prepared by
blind programmers, I. Buslowicz and S. Jakubowski within projects carried
out by the Laboratory of Computer Science at the Polish Association of the
Blind. Nearly all the traditional German printing machines have been
removed from our printing house and replaced by computers. Since most of
our copyists are visually impaired, it has become necessary to provide them
with braille displays. Blind transcribers with their thorough knowledge of
the braille system are entrusted with all difficult texts, particularly
those requiring the use of special braille notations such as the
mathematical, musical or phonetic one. Sighted transcribers are most
frequently given texts assigned for prompt publication, e.g. periodicals.
Both groups of copyists, however, enter texts under Wordstar Professional
since this text editor complies with the following terms:
a. The editor works in the character mode allowing for the application of
braille displays or speech synthesizers, without which the employment of
blind transcribers or proof-readers would not be possible.
b. There is a special program called Wschange which makes it possible to
arrange the edited text according to a braille page size.
c. Wordstar Professional allows for the entering of your own instructions
under so called dot commands or four user's commands. This trait is
particularly helpful when we want to introduce some conventional
instructions into a braille page formatting program.
Brajl program designed in 1989 is constantly being improved. Its main
functions include: the conversion of texts written under Wordstar
Professional as well as ASCII files into braille, the control of Puma-V and
Braillo 400 printers for such parameters as page size, spacing between
braille lines, page numbering, number of copies etc. The program is also
responsible for word hyphenation, making tables of contents, proper layout
of footnotes and tactual representation of inkprint signs by braille dots.
This year our printing house has started publishing large print
periodicals. Both, large print and braille versions are obtained from the
same data stored on a diskette. text files are processed by the Polish
Desktop Publishing type program called Cyfroset, which provides for the
arrangement of the large print text. Photographs have to be glued onto
paper. Drawings in black and white are read by the scanner and incorporated
in the text by the above mentioned Cyfroset program. The original of the
text is prepared with the use of a laser printer on a special kind of
transparent sheets. It is used then as the source material for offset
printing.
To conclude, it is my strong belief that this short review of the latest
developments in the field of computerization to the benefit of the Polish
blind community has highlighted considerable progress marked during the
last few years in our country. Some of our experiences may appear useful
for those countries who have just started the process of applying computer
science and microprocessor-based devices in the rehabilitation and
education of the blind.