Braille, Moon and large print workstations developement

John Kaplin

1. Background

RNIB has been producing braille by computer assisted methods since 1969. In
October 1978, to coincide with a move to a new site, a considerably
enlarged
and more sophisticated system was installed. Ten years later similar
circumstances prompted another computer-based production system. This third
system, and the experiences that led RNIB to it form the basis of this
paper. The author was closely involved with the implementation of the mark
II system in the mid-'70s and was responsible for co-ordinating the
development of the current system.

The first computer system used by RNIB to assist in braille production
consisted of an 8k byte IBM mini-computer fed by punched cards. A volume of
braille of approximately 130 pages took about 2 hours to translate and
format. As output another pack of punched cards was produced which were
used to drive a modified manual metal plate embossing machine. An extremely
labour intensive procedure, this method of production was only used for
standard texts, most braille production was still carried out by
traditional manual methods.

In early 1977 a working party started to put together a specification for a
new system, to be installed at a new production site. The system that was
installed consisted of a twin mini-computer configuration supporting 16
VDUs on each processor.

Also included, along with the usual peripherals such as disk and tape
drives and printers, were 4 braille editing work-stations with A3 size
portrait orientation screens able to display a full page in a large braille
screen font. These QVECs were adaptations of CAD systems using a custom
built keyboard, including dedicated brailling keys, and bespoke software.
The devices were originally intended as editing stations, to be used for
final tidying-up of braille work but they proved to be the most reliable
and the most popular and were extensively used for originating braille.

Original braille input was carried out using bespoke stand-alone devices
known as BCTs (Braille to Cassette Terminals). These BCTs consisted of a
Perkins-like keyboard and a small cluster of control keys together with a
six line 40 character braille display. Output from these devices was via a
standard data cassette tape and files could be loaded onto the mini-
computer for editing on the QVECs. Unfortunately, the BCTs did not have an
editing capability, nor were they sufficiently reliable. As a result they
were the first elements of the system to fall into disuse.

Text input for computer translation into braille was via the VDUs attached
to the mini-computer. An in-house data-entry programme provided for input
and
editing. A verification facility was also available but not widely used. As
text was keyed from a source document formatting codes were inserted as
appropriate. The data was then translated into braille via a version of the
DOTSYS program running on the mini-computer. Corrections were applied
either to the braille file via the QVECs, or to the original text prior to
retranslation. Corrections to the ASCII version of the braille file were
also possible using a text editor on the VDU.

Final braille ASCII files were output from the mini-computer on data
cassettes to drive modified versions of the original plate embossers used
in the earlier card-based system. On-line production-scale braille
embossers such as the RESUS 14 and Braillo 270 were also incorporated
during the life of the system. The RESUS embossers replaced and
supplemented ageing LED 120s which had been used for short runs and
proofing copies since the early days of the system.

A Kurzweil Data Entry Machine was a later addition to the text input
process and supplemented the VDUs. With the KDEM able to handle standard
text the typists at the VDUs could deal with work demanding more
complicated formatting instructions.

As a development of these systems in 1987 micro-computers started to be
used for braille transcription and subsequently for text input. IBM
compatibles were not involved at this juncture, but BBC micros which were
used extensively in education at that time and for which suitable software,
including a braille screen font and six-key chording facility were
available. These systems provided RNIB with a good stop-gap solution whilst
a specification was developed for a replacement system.

Moon is an embossed system of characters, larger than braille cells and
more closely resembling print letters, which also has contractions for
commonly
used letter sequences. At this stage Moon was still being produced by
traditional methods i.e. Moon characters were set by hand in a similar way
to "hot-metal" in the print industry. The pages were then pressed onto wet
manilla paper to impress the shapes and then the paper was carefully dried,
an extremely laborious process.

The opportunity to modernise Moon production in line with braille and in
some way compatible with it was added to the requirements specification. It
was planned that the Moon production system would be relocated to the
Peterborough site at the same time as braille production moved.

Large Print had not featured in RNIB production but was recognised as an
area for which there was potentially a large demand. Large Print readers
are able to obtain copies of popular books through normal sources but there
was no facility for providing such things as information sheets or
brochures in appropriate font sizes. This capability became a requirement
also. At least this was something that standard software should be able to
provide.

2. Requirements Overview

The objective was to provide a work-station able to facilitate all of the
steps involved in the preparation of texts for production in any or all of
the media proposed.

The steps involved are:
- Text Input/Editing
- Braille Input/Editing
- Moon Input/Editing
- Translation of text into Braille or Moon
- Large Print preparation
- Archiving
- Networking

A major consideration was that, wherever possible, standard commercial
software and hardware should be used with the minimum of bespoke
development.

The potential benefits from compatibility with other producers of reading
materials for the visually handicapped was borne in mind in designing the
new systems. Transfer of data to other organizations for local
printing/embossing is likely to be as useful as receiving data from outside
producers.

Tactile displays and/or speech output are necessary if visually handicapped
users are to have access to the systems.

2.1. Text Input and Editing

Keyed input using a commercial package. This route would be particularly
relevant to text which is not suitable for Optical Character Recognition
(OCR).

OCR origination using the KDEM or a similar system. Editing to be carried
out using PC based text processing software. This would be primarily
concerned with preparation of text for braille and Moon translation.

Data coming from external sources e.g. compositors tapes, CD-ROM, home
volunteers, other organizations and other sources (including PRESTEL,
TELECOM GOLD and other data communications systems).

In order to facilitate maximum flexibility, wherever possible corrections
should be applied to the text file and re-translation into the appropriate
medium carried out.

2.2. Braille Input and Editing

The system should offer the options for input via a chording sequence or
QWERTY keying:
- using a software modification such as the "SIX" program to enable the
home keys of a standard keyboard to be reconfigured as the braille keys, in
the style of a Perkins Brailler, for those braillists who prefer this mode.
- using the braille ASCII character set for direct input of grade II
braille via a standard keyboard.

The display should be capable of depicting the braille either in a six-dot
matrix form or as the ASCII representation of the braille characters. The
ability to display the complete braille page would be highly desirable, as
page layout etc. are often important. An A4, or portrait orientation screen
may be appropriate.

2.3. Moon Input and Editing

In a similar manner to the braille system Moon can be input on a QWERTY
keyboard using the ASCII equivalents of the Moon characters and either a
Moon font or the ASCII generated on the display.

2.4. Translation into braille or Moon

The braille translation software should be capable of producing a reliable
close approximation to grade I and grade II Standard English Braille from
texts originating from any of the in-house sources. Integration with the
text processing software should be developed to minimise the amount of
formatting information required to be added to the text. A facility for
translating braille into print text would also be a useful facility, though
not essential.

An equivalent program for converting the same text into the appropriate
Moon codes would also be required. An earlier project under the auspices of
Dr John Gill developed a Moon translator which adhered to the rules imposed
by the use of the Boustrophedon effect (bi-directional reading facility). A
decision to no longer implement the Boustrophedon should simplify the task
of
translation.

2.5. Large Print

Text which has been prepared for tactual production routes should also be
available for print production, either before or after insertion of format
codes. Compositors tapes and CD-ROM are likely to be particularly relevant
to this application.

Although there is a trend towards Desk Top Publishing (DTP) in the PC
environment, and the top-end packages offer a high level of sophistication,
it may be preferable to incorporate a professional type-setting system.
This would enable RNIB to handle most of its printing in-house e.g. forms,
headed stationery etc. with the appropriate cost savings.

2.6. Archiving

It should become practice to commit to archive various forms
 of the data e.g. clean text, translated but unformatted braille or Moon,
finished data. For this purpose a high density archive medium should be
considered e.g. WORM technology CDs. The fast access, security of data and
compactness are benefits when compared to magnetic tape.
A. regular regime of backing-up data onto streamer tape or disks will need
to become part of the system operation.

2.7. Networking

The 30+ work-stations are designed to function as stand-alone production
units able to work in any medium and support any output device. For reasons
of economy and efficiency it is preferable to allow a sharing of resources.
To this end it is planned to connect the work-stations and the various
input and output peripherals.

Clusters of 4 to 6 work-stations will probably be preferred, in order to
permit more effective supervisory control.

The proposed work practice will involve downloading the particular document
from the central file-store to the hard disk on the work-station from where
it can be edited or translated without imposing any processing overhead on
the file-server. On finishing a work session, or a job, the file will be
transferred back to the file-server from where it can backed-up or archived
centrally. Embossers, printers and plate-makers can be attached to work-
stations around the system or to dedicated PCs on the network.

If commercial typesetting systems are to be integrated with the other work-
stations on the network they may influence the choice of network topology.

3. Evaluation

3.1. Bespoke Option

A specification for a custom designed and built work-station to emulate the
very popular QVEC editing stations was commissioned but was not adopted,
partly on grounds of cost and partly as a result of disappointing earlier
experiences with BCTs, ie the potential problems of on-going support from a
small specialist company. There did not appear to be anything suitable on
the market, particularly from the point of view of braille displays and
suitable keyboards. It was at this point that it was decided to forgo the
luxury of a QVEC-style full screen display and compromise on a PC based
system. Exploration of the potential for a bespoke software solution led to
a similar conclusion re long term development and support, and also the
time scales involved seemed unattractive.

3.2. Software

The objective then became to use a standard package to cover all aspects of
input and editing in any of the media involved. Evaluation of software
against a set of criteria produced a short-list of options:

1. A text editing package from dolphin systems for the disabled which had
an excellent braille display but was not designed for page based
applications and as such had short-comings for the type of work involved

2. A word processor called ChiWriter designed for scientific applications,
which has a font designer built-in. This piece of software also had its
limitations, a serious one was the maximum of 100k bytes for a data file,
this limits braille files to approximately 90 pages, well short of the 130
or so pages of the average volume. Headlines at the top of each page are
not handled satisfactorily either in Chiwriter as there is not the
"running-head" feature found in most commercial wordprocessors.

3. A system based upon WordPerfect with an add-in braille font. A number of
font add-ins were investigated along with several of the leading commercial
word-processing software packages. At the time WordPerfect version 4.2 was
being used elsewhere within RNIB as the standard wp package.

The WordPerfect option appeared to offer the greatest potential for
satisfying the criteria, for text processing in each of the media required.

3.3. Hardware
It had already become apparent that successive generations of software were
demanding ever more powerful hardware to support them. As a result it had
been decided that Intel 80286 based micro-computers would be the standard
machine for general use. Although WordPerfect v4.2 will run happily on an
8086 level micro it is a little slow, v5.0 is rather hampered by the limits
imposed at this level of computer power. As further development proved,
even a reasonably fast and enhanced 80286 machine is at full stretch to
handle to requirements that the braille aspects of the work-station impose.
For the type-setting aspects of large print production it was decided to
step up a level of micro-processor power and employ computers based on
80386SX chips.

4. Development

4.1. Text

Text derived from KDEM files is edited in preparation for translation into
braille and, in future, Moon. Similarly, texts from other sources can be
prepared for further production processes. WordPerfect has the facility for
accepting ASCII files, and a variety of options are available for
converting files from other sources into WordPerfect formats. The powerful
macros facilities available make editing reasonably straight-forward.

4.2. Moon

The implementation of a Moon input system commenced with the development of
a Moon font for WordPerfect to drive a laser printer. The software was then
configured to make the font available for A4 and B4 landscape paper. Text
was able to be keyed in using the appropriate characters to represent the
contractions and allowing the wp software to handle the pagination. Moon
does not have headlines as braille does, but pages are numbered. At this
stage of development a number of page numbering schemes were tried out:
having the page number on a line on its own, but this was wasteful of paper
in a bulky medium; using a prepaginated columnar set-up and importing the
Moon text into it; manually applying page numbers to the finished pages
before final embossing. None of these was totally satisfactory and it is
only recently that a facility for positioning the page number at the right
hand end of the first line of text has been implemented. The Moon text
input and editing scheme was originally developed in WordPerfect v4.2 and
only upgraded to v5.0 when it was integrated with the braille system. At
this time a new version of the Moon font was developed to improve the
quality of the printed output.

From the laser printer output of the Moon pages of text a Minolta copying
system using "swell paper" was originally used to produce the final
embossed output. Because of the cost of "swell paper" production of Moon by
this method was limited. A photographic system is now used to produce
polymer masters from which pages can be pressed in a similar way to braille
pages. As far as the wp aspect is concerned there are no real differences
between Moon and standard text other than the font involved.

The image-setter supports the Postscript printer language and both braille
and Moon Postscript fonts have been designed in-house. Moon is now being
produced in WordPerfect using the PostScript Moon font and output to the
image-setter, this now accounts for about 80% of the image-setter's
capacity.

4.3. Braille

Development of the WordPerfect based braille system was delayed by several
months during the transition from WordPerfect v4.2 to v5.0. This was
principally due to a delay in development of the font designer FONTMAX in a
version for the new release of WordPerfect. The improvements and
enhancements available with v5.0 had the potential to provide a much more
sophisticated system and so the delay was endured. One of the major
advances offered by WordPerfect v5.0 was the facility to preview the page
as it would look on printing, including headlines and page numbers in situ,
and FONTMAX provided this in a braille representation. This is essential as
there is no headline shown on the text editing screen.
One of the drawbacks of both the ChiWriter and WordPerfect braille systems
is that they are not able to use the 40 column mode of the PC, so the
braille characters only use half of the screen and are not as large as
would be liked. On the other hand, with a colour screen, WordPerfect offers
the option to select from a palette of colours to suit your own preference
for background and foreground. Some amazing combinations are possible!

A chording program, "SIX" from dolphin systems for the disabled was
originally used to reflect the usage of "Perkins-style" keyboards to
produce the braille cells. This program only applies when CAPSLOCK is
active, so allowing responses to prompts from the software to be entered in
either braille characters or print.

The first evaluation version of the braille aspect of the work-station
employed macros assigned to ALT-key combinations to provide shortcuts or
braille-specific facilities. This approach was refined as a result of user
feed-back and was greatly improved by using the WordPerfect facility to re-
map the keyboard and so assign new functions where appropriate to
WordPerfect use of function keys. A list of the function key assignments is
included as an appendix to this paper.

The system as described is demanding of computer resources. WordPerfect
alone requires 384k, including FONTMAX takes the memory requirements upto
400k. The addition of the "chording" means that 425k of the 577k available
after DOS has been loaded is accounted for and only about 150k is available
for data. This may seem adequate for most purposes, but the later addition
of network software will reduce that figure by a further 70k. On top of
this each braille character takes up 4 bytes of memory, as it consists of
both a start and end byte around a character set value and the actual
character value within that character set. In this arrangement the standard
130 page volume, which takes up perhaps 100k in ASCII characters expands to
maybe 350k in braille dot format. Using the hard disk for overflow files,
as WordPerfect does by default, results in frequent disk transfers of
blocks of data and also produced corruptions of data on large files. The
addition of 512k of extended memory to each workstation and assigning it as
a RAMDRIVE for use by WordPerfect produced a major improvement.
Unfortunately, it did not completely solve the problem. On occasion, for no
apparent reason, a data corruption will occur which results in out-of-range
characters being generated. Attempts to delete one of these characters
frequently results in a proliferation of invalid characters and tracts of
braille are no longer accessible, in effect lost. This is obviously not
good for users' morale, but investigations are underway to identify the
cause and determine a solution. Apart from this serious problem the system
is generally well liked by users.

4.4. Large Print

Although a Desk-Top-Publishing package could produce the type fonts etc
that are required for large print readers, there was a requirement to drive
an imagesetter to produce the quality of output necessary for the
anticipated printing demands. A number of type-setting systems were
evaluated, based on all manner of computer platforms. A decision was made
to install a Hell-Zenotron image-setter and to front-end it with software
called 3B2, PC DOS based, readily networkable and compatible with
WordPerfect.

4.5. Translation Software

A number of braille translation systems were evaluated to determine the
most suitable for RNIB's requirements. Some of the features of "house
style" which were required were not available, although modifications were
offered by suppliers. In view of the anticipated changes to the braille
codes likely over the coming few years it was decided that an inhouse
solution may be appropriate. At the same time as the evaluation was taking
place a project to develop a music translation system was also underway. As
text to braille translation was to form an essential part of the music
system, it was decided to develop that aspect as a priority to provide the
required software. Using the DOTSYS software from the mini-computer as a
starting point a new version of the translator was written in the "C"
language for the PC. As well as music it is planned to add mathematics and
science codes t the text and computer braille currently available.

A translator for text-to-Moon has recently been developed and is currently
undergoing testing. This translator is compatible with PC-DOTSYS in that
the same formatting codes are used.

Also under development is a project to develop a "front end" to facilitate
easier conversion of text to braille and, in due course, Moon. This will
provide for recognition of text formatting information in its native mode
in a number of leading word-processing packages.

4.6. Bespoke Work-station Features

Apart from fonts supported and page formats the Moon aspect of the work-
station does not require any adaptation from the standard WordPerfect
package, nor does the print application. The braille implementation
represents the major adaptation and a summary of the function key
assignments is presented as an appendix to this paper. An explanation of
some of the features should help to clarify the rationale of the system.

Many of the standard features available in WordPerfect are not applicable
to braille, such as Bold and Underline etc, so where appropriate the
function key assignments were changed to braille-specific or useful
functions. In several instances the opportunity to shortcut several levels
of WordPerfect's sub-menus was taken, eg defining headers involves 5 levels
of menu choice - a
function key now takes the user straight to the header input screen. The
same function key in conjunction with the <Shift> key offers the most
recent header for editing.

A major problem with the FONTMAX add-in to WordPerfect is that is does not
allow Search and Replace in the font selected. To counter this it was
necessary to provide an alternative set of functions to perform these
operations. In order to facilitate Search and Replace it was necessary to
use the second document feature and assign the string to be searched for to
an internal variable which could then be used as a parameter to
WordPerfect's own Search function. This was extended to assign a braille
string to a second variable to facilitate the Replace feature. Although not
ideal it does work! A side-effect of having to develop enhanced functions
is that sometimes they could prove to be fragile with the result that a
number of alternative keyboards were designed which limited options to the
user in order to minimise the risk of crashing the system. One of these
keyboards is specific to the on-line "help" system provided - again using
the second document feature, but limiting the user to browsing the screens
of information and exiting. Even this is not totally fail-safe so there is
an option on every bespoke alternative keyboard to return to the standard
default WordPerfect keyboard from whence a restoration of normal service
can be achieved.

Some function keys are dedicated to simplifying implementation of RNIB/BAUK
"house style" features, such as the 3-space paragraph used in magazines.
This is achieved by using the "hard-space" character which prevents word-
wrap between words. In effect 2 "hard-spaces" are linked to the word that
follows, thus producing the cell-3 start to a standard paragraph if the
whole string is carried down to the following line.

Another of the "house style" features involves the use of print-page
numbers in the braille text. Standard practice is to include the current
print-page number at the left of the headline and whenever the print-page
number changes an indicator, consisting of a dot 5, dots 2 and 5 and then
the number, should appear centred on a line on their own at the precise
point of the print-page turn. By the use of a function key the user is
prompted to enter the new print-page number and then both the headline
element and the in-text element are generated automatically.

As mentioned elsewhere, the headline feature in WordPerfect is widely
appreciated but it does have one quirk, which does not apply in braille,
which is that a blank line is generated to immediately follow the headline.
This blank line is removed via a tidy-up program later in the process, but
it does mean that the line-count is always 1 line out on the editing
screen. Another function of the tidy-up program is to convert the page
numbers assigned by WordPerfect, as it paginates, into the equivalent
braille numbers.

Because of the way in which the WordPerfect/FONTMAX combination stores the
braille characters it is necessary to convert them into ASCII before they
can be used by braille devices. WordPerfect provides an ASCII printer
called Dos Text Printer which combines the page information with ASCII
text. Editing of the character tables for this printer driver facilitated
the conversion of the complex internal representation of the braille into
ASCII values. By printing the file to disk and then running the tidy-up
program outside of WordPerfect a standard ASCII braille file is produced.
The printing to disk would normally involve delving through 4 levels of
menus to achieve but is available on the function key that WordPerfect
normally assigns to "Print".

If dot representation on screen is not required the same function key
features are available to users working with ASCII braille characters, the
original WordPerfect Search and Replace functions are then available. If
"chording" is not required ASCII input of grade II braille using the normal
keyboard can present the characters in dots or not as required. The ASCII
display can be used by visually handicapped people via a tactile display -
speech output is not ideal for ASCII braille.

The facility to take an ASCII braille file and convert it into a
WordPerfect/FONTMAX file has also been incorporated. Not a lot of use has
been made of this facility as yet, probably because it takes more than an
hour to convert a standard volume, including handling extraction and
encoding of the headlines. This option has been used where extensive
editing has been required on a file for which only the ASCII version is
available, as users tend to prefer to edit in braille dot format. Files
archived from the old mini-computer system also come into this category.

5. Future Enhancements

The serious problem of system overload generating out-of-range characters
is the top priority. In an attempt to cut down the number of programs
involved the replacement of FONTMAX is being evaluated. WordPerfect offers
the facility to redefine the screen character map and it has been possible
to produce the appropriate braille display mapped onto a new keyboard.
Still to be achieved is a page-preview in dots and the chording facility
for six-key input needs to be modified to accept the new set of key codes.

6. Archiving

Because of the non-volatile nature of completed texts it was decided to
implement a WORM drive for long-term archiving. The 400mb capacity per disk
is great improvement over the 800 bpi tape that was used previously. The
direct access ability of the WORM is another advantage over magnetic tape,
even though access times are slow compared to disk drives. Magnetic
streamer tape is used to back-up the hard disk on the network file-server.

7. Network

A Novell Netware 386 system was installed in April 1990. The features of
the network are:

- To enable upto 50 users of the transcription workstations involved in
producing braille, Moon and large print to have access to shared resources,
primarily braille embossers and laser printers
- To have centralised filing of data and a common library of macros and
menus for the WordPerfect based system
- To facilitate management of data files for archiving and backup centrally
- To provide a production monitoring system using a PC database, accessible
to upto 20 users in Production Control, Production management and Marketing
- To allow upto 10 users in the Editorial and Proofreading departments t
have access to aspects of the system
After a few teething problems the network is now functioning to
specification.

Each transcription work-station has its own copy of WordPerfect v5.0 but
uses the file server for file storage and as the source of all macros and
bespoke keyboard layouts. This ensures that everyone is using the same
version of the macros etc. It was not possible to implement v5.1 of
WordPerfect as FONTMAX was not compatible with it. Version 5.0 was no
longer being supplied when the network was implemented so a fully networked
WordPerfect system is not currently available.

8. Summary

The objectives have, for the most part, been achieved,although there is
still some work to be done in resolving the intermittent out-of-range
character problem.

I would like to acknowledge the help of my colleagues, and also thank them
for their patience!

9. Appendix

Braille Work-station redefined Functions

<F1> cancels most operations. Do not use with the search and replace
functions. To abort search or replace enter just <CR> at each prompt.

<Shift F1> facilitates screen colour customisation. Press <CR> when
finished. Serious damage to your, and other people's, sanity may result
from inconsiderate use.

<F2> to use the search facility when in braille display mode. <CR> is the
terminator.

<Shift><F2> to search backwards through the file. <CR> is the terminator.

<ALT><F2> to enable search and replace in braille display mode. <CR> is the
terminator.

<F3> help screen.

<Shift><F3> to change the braille page number. Enter the number in regular
text. It will be converted to braille by the tidy-up program.

<Alt><F3> reveal codes. <F11> does the same.

<Ctrl><F3> to refresh the screen (if major reformatting causes temporary
problems).

<F4> positions the margin 2 cells in and all run-overs are at that cell
until the next <CR>.

<Shift><F4> Produces a 2 cell indented run-over.

<Alt><F4> turn BLOCK on. <F12> does the same.

<Ctrl><F4> will move the marked Block. Move the cursor to position you want
text to be moved to and press <CR>.

<F5> Lists files in the default directory

<Shift><F5> for inputing print page numbers at the top left of the page.
The dot 5, middle C is also centered on the current line with the braille
number that you enter.

<Alt><F5> edit headline element of print page number. The cursor must be
after the defined headline.

<Ctrl><F5> will copy the marked Block. Move the cursor to position you want
text to be copied to and press <CR>.

<F6> allows for 12 centered characters - enter the character you want
centered. Terminate with <CR>.

<Shift><F6> centre characters until <CR> is pressed.

<Alt><F6> Flush right - terminate with <CR>.

<F7> Exit.

<Shift><F7> copies the current screen file to a file on the drive entered
as a response to the prompt, with the file name you supply at the second
prompt. Do not give the file an extension, a default extension of .BL is
generated automatically.

<Alt><F7> displays the printer control screen. If after issuing the print
function <Shift><F7> nothing appears to be happening, check the print
status and cancel the job or ask for help.

<F8> for inputing a centered headline - press <F7>
to exit!

<Shift><F8> for editing a headline. The cursor must be after the defined
headline. Press <F7> to exit.

<F9> gives three centered asterisks.

<Shift><F9> gives a three space paragraph.

<F10> save file: it is recommended that you save before "printing", just in
case anything goes wrong!

<Shift><F10> retrieve a file. The default directory is on the file-server.

<F11> reveal codes. The same as <Alt><F3>.

<Shift><F11> to preview page.

<F12> turn BLOCK on. The same as <Alt><F4>.