Monocell Braille line for IBM PC and compatibles.

A.Parreno and P.J. Magallon

Abstract

The monocell Braille line described previously (1) as integrated in a data
proccesing device, has been redesigned to make a stand alone line capable
of being used as a Braille display for the IBM PC and compatible computers.
In the monocell Braille line, a single cell replaces the 40-80 cells of a
conventional display, since it can take the place of each one when it is
displaced by the reading finger along a rail on the display.
At each of the 40-80 positions the cell could take, their pins rise
accordingly, displaying the caracter corresponding to this position.
In this way, when the user puts his finger on the cell and makes it glide
along the display, he perceives each successive character in its right
position on the line.
This result is due to the action of a position detector whose information
determines which character is going to appear in Braille form on the cell.
The computer display for the blind requires only a card that is plugged
into a free slot of the PC.

(1) Parreno, A. A Virtual Braille Line for a Paperless Braille Device.
Workshop on "Techniques and Devices for the Blind", Florence, November 28-
30, 1988.