Electronic Newspaper System for Visually Handicapped People.

O. Sueda, K. Kato and Y. Oosaki.

1. Introduction

At present, the quantity of information, which can be obtained in the form
of braille or speech by a visually handicapped person in Japan, is not
satisfactory.   In case of the important information source "newspaper",
many services such as reading service, database system for personal
computer networks and so on have been prepared.   Although a visually
handicapped person can receive the above services, his situation is
different from that of a sighted person in timing, quality and quantity.

Research on the broadcast system for newspapers using FM radio frequency
has been done in Sweden1).  We think this broadcast system is useful as a
new method of publication service for visually handicapped people.

The target of our research is to develop a Japanese data broadcast system
for visually handicapped people in Japan.  In this system, the cable
network for music broadcast of Osaka Yuusen Housou Co. Ltd., which has 440
channels, is used as the means of transmitting data.

2. Data receiver for Japanese

In our electronic newspaper system, a partially sighted person is also
considered as a user, the same as a blind person.  A receiver has been
designed which has the functions of braille display, synthetic speech and
expanded display of the text on a monitor television.

In Japan, ordinary texts are a mixture of letters from the English
alphabet, Greek letters and symbols of mathematics and chemistry, the two
Japanese phonetic alphabets (hiragana and katakana), and several thousand
Chinese characters, or Kanji.   On the other hand, the textbooks used at
schools for the blind are written in the Japanese phonetic alphabets
without Kanji characters, which are the main elements of Japanese in
ordinary books.  In a Japanese sentence, many compound words of more than
two Kanji characters are used and there are many phrases with the same
pronunciation, although their meanings are different.   Therefore, simply
hearing a Japanese sentence sometimes brings about misunderstandings and
reading a Japanese sentence written in the phonetic alphabet brings about
more misunderstandings because of the lack of accents and/or rhythms.

The Kanji braille codes were invented by T.Kawakami in 1969, and developed
for educational purposes by Mr. and Mrs. Kawakami.   The expanding braille
code system to express assorted letters, symbols and graphic patterns was
developed by O. Sueda (1985)2), including Kanji braille.   In the new
braille code system, free combination of various mathematical, physical and
chemical symbols, and music scores into normal Japanese sentences, as well
as writing computer programs, is possible.

The data receiver for Japanese sentences should prepare the character
display devices, or device, for the Kanji characters in ink-print and/or in
braille.  The synthetic speech device is also useful as a supplementary
device

3. Problems of transmitting newspaper data

There are three big problems in the transmission of newspaper data.  The
first is how to protect the copyright; the second is how to increase the
reliability of received data against noise; the third is how to edit the
news to maintain readability in baille.

In Japan, print translated into braille from ink-print is free from
copyright.   The number of receiver will be more limited than that of the
system developed in Sweden because of the use of a closed cable system
compared with FM radio broadcast.   However, in case of the electronic
braille newspaper system, we transmit the data by usual computer code which
is readable by the sighted person on a monitor television.   In order to
solve the first problem, the receiver is numbered by the hardware, ID
number, which is used to open the gate according to the electronic key
which is transmitted precedently for the main data to the registered
receiver, and the data is ciphered/deciphered for transmitting/receiving by
the electronic key which is changed daily.

How to transmit data reliably is the general problem of communication.   In
our cable system for music, each channel has several KHz band widths and
for digital signal, the reasonable speed of transmission is about 4,800
Bauds.   The morning newspaper has about 300 kilo bytes of data and about
ten minutes will be neccessary to transmit all the data.   The data is cut
into blocks of 112 bytes and transmitted with a block check code.   The
whole of the data is transmitted three times.   The block of data which has
errors is omitted and filled by null data at the first transmission, and
that block will be filled by correct data at the second or the third
transmission.

A weather forecast and a table of TV programs are also very interesting for
visually handicapped people.   However, these items are not produced in
text format and it is very difficult to display them in braille or in
speaking.   An advertisement column is also very useful for handicapped
people.  However, its block copy is made by photograph and no text data in
newspaper file, although it is constructed just by characters.   A
financial column includes many tables as data and these tables are very
difficult to translate automatically into braille.   Some editings and some
rewriting of news is done at the braille printing house before
transmitting, in order to facilitate the automatic translation into braille
at the receiver side.

4. Hardware of the electronic braille newspaper system

An electronic newspaper publishing system is made up of a personal computer
system and a modem box for transmitting.   An electronic newspaper
receiving system is made up of a receiver for cable broadcast, a modem box
for receiving and a personal computer system for the visually handicapped
person with a braille keyboard, a braille display unit, a synthetic speech
unit and a braille printer.   The modem box for transmitting data has the
functions of ciphering of data according to the key code and producing of
quasi X-modem protocol.   The modem box for receiving data has the
functions of an electronic key for protection of copyright against non-
registered receivers and deciphering of data.   Each receiving modem box is
numbered by hardware, ID number, for controlling of opening/closing of the
deciphering circuit and data rearrangement function.

5. Software of the electronic braille newspaper system

The data of the morning newspaper is mailed at the braille printing house
of Nippon Light House early in the morning, at 2 or 3 AM.   At first, the
data is automatically cut into each news file with the header, which
containes attributes of the news such as column number, page number of
original ink-print and a number of news items.   A control data file is
produced every day which is transmitted precedently for the main data of
news, constructed by the electronic key data for cipher/decipher and
receiver control date according to the ID number of each receiver which is
registered for reading the newspaper.   The small amount of editing of news
is done manually by the professional staffs of braille translation at the
printing house.   After these arrangements are finished, the control data
file and main data files are sent three times to the transmitting modem box
connected to the transmitter of the special channel of cable broadcast for
visually handicapped people.

A receiver wake up according to the control data is received precedingly
for the news data, if it is the registered receiver.   The news data is
deciphered according to the decipher key data, and sent to the personal
computer by a block data with the RS-232C serial port.   On the personal
computer, blocks of data are gathered up and formed into a news file, and
it is saved in a floppy disk.   If an error occurred during the first
receiving of data, the errored block of data is omitted and filled by null.
At the second or the third period of receiving, the block of data, which
would be error free, is inserted into the old file.   The probability of
missing the same block three times is designed in a very small value,
p=(0.0088)3=0.00000068, and the total number of blocks are about three
thousand.

The user of the electronic newspaper system can read the news data in the
morning with the reading program in braille display and in speaking and can
print it out in braille.   At first, the user selects the page and secondly
selects the news guided by the title and the abstract.

6. Conclusion

In Japan, the cable broadcast system covering almost all Japan is operated
by one big company, Osaka Yuusen Housou Co. Ltd., and one of four hundred
forty channnels is used for visually handicapped person to send the news
and to read the newspapers.  This situation is of benefit to the
development of an electronic newspaper system.  According to this research,
many problems are also revealed, such as the rewriting of tables, omitting
of the graphic news in advertisement columns, the use of special Kanji
characters out of the standard code table, mainly for the name of persons,
and so on.

This research has been conducted as a joint project with Naruto University
of Education and Nippon Light House by the fund from Mitsubishi Foundation,
1988.

The Asahi newspaper Co. Ltd. and Osaka Yuusen Housou Co. Ltd. have also
assisted this research.

7. References

1) H. Rubinstein : Radio-Distributed Digital Daily Newspaper for the Blind,
Proc. of 2nd Int. Conf. on Rehabilitation Eng., pp583-584, 1984.
2) O. Sueda : Eight-dot Braille Code and Automatic Braille Translation
Boards, Proc. of 5th Int. Workshop on Computerized Braille Production,
pp273-303, 1985.