Telebanking Systems & Intelligent Houses for the Visually Impaired.

Gerrit Van den Breede.

1. Introduction.

In todays world, we can see that the use of electronic data communication
is rapidly growing and many different systems are used. Special computer
networks, often based on X.25-systems, or wireless systems do exist, but
the telephone network is the most widespread and universal one. More and
more services become available by telephone: security systems, data bases,
tele-work/study, tele-library, Auditel-systems and Bulletin Board Systems
(BBS). Like everyone, Visually Impaired Persons (VIPs) start using more and
more high-tech equipment ie personal computers (PC's) in combination with
modems. More work can be done without leaving the house. During the
Workshop on Intelligent Houses (IH) for the Blind1 several aspects of
Intelligent Houses were discussed. These houses are developed by the
electronic industry to serve the general public.and they can contribute to
the comfort of modern living. An Intelligent House can help the visually
impaired to have a more independent live. We are going to discuss a few
important aspects about IH for the blind.

2. Telebanking.

VIPs (Visually Impaired Persons) always need assistance when they go into
traditional banking matters. For them, it's difficult to fill in the
documents or to know the amount of money on their bank account. Privacy was
not possible.

We shall use the word "Telebanking" for the set of automated services of a
bank towards its customers. Originally, these services were set up for
small and big companies to handle their banking operations in a more cost-
effective way. We will discuss the accessibility of these services by the
VIPs.

Starting with the ATM's (Automatic Teller Machines), telebanking became
reality for the general public. These ATM's are very hard (practically
impossible) to use for VIPs because of various reasons like eg the use of
cartoon-like coloured graphics, different types of keyboard lay-out, lack
of appropriate output (braille or speech), ... InfoVisie is stimulating our
national telephone company (R.T.T.) for the introduction of a special radio
frequency for use by the VIPs.  Low power transmitters in the cash
dispensers (but also in traffic lights etc.) can give the necessary
information to a small receiver (eg with an earphone) carried by
handicapped persons. This topic is also discussed in the "COST 219" group,
a European Research group on "Telecommunications for the Handicapped".

The BBL (a Belgian bank called "Bank Brussel Lambert") started in 1981 a
telebanking service via telex. About six years ago, banking via
asynchronous modems was started by different banks, but the real expansion
started in 1988. Therefore we made a study to know:
- the types of public telecommunication systems that are used by the banks
:
  * Videotex.
  * X.25 (called DCS in Belgium, Transpac in France etc...).
  * BBS (private Bulletin Board Systems).
- the type of protocol that is used :
  * TTY.
  * VT52/VT100 or other ASCII.
  * Videotex/Prestel, Minitel/Teletel, Bildschirmtext/BTX-CEPT.
  * or others.
- which protocols could be made accessible by VIPs using a PC with
enlargement software or a brailledisplay.

2.1. Possibilities of Telebanking systems.


____________________
1 Within the framework of the "Concerted Action on Technology and
  Blindness", the Workshop on Intelligent Houses (IH) for the Blind was
  held in Maastricht (NL) on December 11-13, 1989. Fifteen papers were
  presented by 29 participants from a number of European countries.

The most important common possibilities of the different telebanking
systems are :
- consultation of your bank-account,
- payment orders (both domestic and external payments, BEF and foreign
currencies, individual and collective operations, with other banks)
- exchange rates/interest rates consultation,
- Multibank option (accounts administration between banks),
- ordering bankpapers (eg cheques),
- to claim balance sheets, bankruptcies and compositions.
For some of these options, an extra fee must be payed. The price for the
standard options varies between free and 25 USD/month.

2.1. Security and standards.

A special encrypting terminal (in Belgium, mostly a TRASEC2 terminal) in
combination with a chip-card must be rented if the money-transfert options
of terminal banking is used. With this personal chip-card (the size of a
credit-card), a limited amount (1.400) of "electronic signatures" can be
given.
PAY 90 is a multifunctional software packet that can be used with different
banks. The packet is exclusively designed for the electronic execution of
payments with maximum security. The payment-authority of different users
within a company can be defined. It works with a TRASEC terminal and the
cost of the PAY 90 packet is ñ1800 USD. For about half that amount, PAY 90
is available without the possibility of sending payment orders by
telephone-line. The payment-orders are stored on diskette which has to be
brought to the bank. Not all the banks are using this PAY 90 "standard",
but most of them accept diskettes with payment orders.
PC-Bank is the name of the most recent attempt to standardization. PC-Bank
is a system that has the possibility to integrate electronic banking-
operations between all banks. The system is momentarily in a testing period
and the only limitation is that a TRASEC terminal can not be integrated.

2.3. COM-COM, interactive telebanking and "Paydisk-systems".

COM-COM stands for COMputer to COMputer connection. This type of connection
is mostly used for transmitting a large amount of payment orders. It
requires a security protocol like TRASEC.
The interactive connection allows you to consult your account(s) and all
kinds of bank information like exchange rates. Security procedures are
necessary if money transfer is involved (TRASEC or signature on paper).
Payment orders can be done without any direct connection with the computer
of the bank. Customers can make payment orders by means of special software
(mostly offered free by the bank) on their own PC. The payment orders are
stored on a floppy disk which has to be brought to the bank3 where a
signature has to be placed for confirmation.

2.4. Telebanking by speaking computer (Auditel).

The working principle is the following ; the user can, by means of a
standard touch-tone telephone call his bank where a special "Auditel"
computer accepts the call. The dialogue starts with a spoken message from
the banks computer (asking the language of the user). The user answers by
pushing the according buttons (producing tones which are detected by the
"Auditel" computer) on his telephone set
The user is guided by a menu-driven system. Every time a connection is
made, a 4-digit password and the number of the bank-account must be typed
in by the user. The password can be changed by the user. After typing these
two numbers you have the possibility to do all the standard manipulations
with your bank-account. Also payment orders from your account to other
banks. Additional services like exchange rates, ordering bankpapers or

____________________
2 TRASEC stands for TRAnsaction SECurity. At the end of 1987, the
  co”perative company Trasec was founded to co”rdinate the system. Trasec
  has arised from the financial institutions inside the CIRI (Centrum voor
  Interbancaire Research en Informatie). The CIRI is the institution within
  the BVB (Belgische Vereniging van Banken, Belgian association of banks)
  for normalisation of informatics.
3 The contents of the floppy disk can also be transmitted by telephone line
  but without security measures. In this case, a signature for confirmation
  is also necessary.

calculation of the monthly rent are available, but not all banks4 are
offering these services.
These "Auditel" systems are more and more used by other organisations too.
One example is TeleCar, a database to look for a second-hand car.

2.5. Special cases.

The "Tiense Bank" introduced a pocket sized terminal with a touch-screen
and a built-in modem. It is battery-operated and can directly be connected
(wall-plug) to the telephone network. All standard bank-account
manipulations can be done. This device can be used by some low-vision
individuals but is not adaptable for blind persons.

3. Intelligent Houses and Telebanking facilities.

Concerning the technical aspect of an IH for the Blind, three main
functional areas can be distinguished in order of priority :
Status Information
Tele-Services
Remote Control

3.1. Status Information.

The IH should provide status information on request about the house, the
environment and the human. A few examples : Are doors and windows closed?
What's the outside temperature? Hart-beat guarding for hart patients.
For VIPs, the alarm/status information should be given in an audible form.
There can be a problem if "private" status information is given by
synthetic speech. It can be a solution that the house "beeps" you (wrist
watch) if status information is present. If you want to here the message
anyway, then you can start it with a trigger button on the watch. Alarm
information should be given immediately.

3.2. Tele Services.

Various numbers of tele-services can be provided by a terminal that is
accessible for VIPs (enlargement system, brailledisplay, tactile graphic
display, speech output) . This terminal can be connected to the telephone,-
cable-TV,- ISDN,- or IBCN-network.
Medical guarding systems for chronically ill patients through automatic
monitoring systems is very important.
A 24-hours tele-helping service for the blind could be set up ; on request,
a remote assistant can look at situations at home (which are to complicated
for blind people to handle alone) by using a video connection.
Telebanking can also be one of the tele-services in an IH. In this case, a
terminal (ie PC + modem), connected to the telephone network is
appropriate. Another (cheaper) possibility is using the standard touch-tone
telephone and call the speaking "Auditel" computer of the bank. This way,
the most common money transfer matters (payments) can be done.

3.3. Remote Control.

Remote control can cause a lot of problems for a VIP. How can he have
feedback? How to know were the Remote Control Unit (RCU) is? How does the
user get feedback from the system? The possibility to switch all functions
of the house to a  stand-by position when leaving the house can be a useful
facility. Another facility is to have automatically presetting functions ;
activating or deactivating functions (temperature, humidity, background
music, ...) at a certain time of the day, week, season.

4. Conclusions.

- All telebanking systems (via PC-terminal) are offering the possibility to
present their screens in a non-graphic way (ASCII). Therefore, the contents
of the screen can be presented in braille, speech or enlarged characters.
- Videotex has the possibility to split the screen in two enlarged parts so
that it may become readable by low-vision individuals.


____________________
4 In Belgium, 3 banks are offering a public "Auditel" system :
  Spaarkrediet, BAC and Generale Bank.

- Telebanking with the standard touch-tone telephone and the speaking
"Auditel" computer is the cheapest and most simply way of electronic
banking. No special high-tech adaptations for the VIPs are necessary.
- Telebanking in an IH can be achieved by using the specially adapted
terminal or the standard touch-tone telephone.
- As an extra bonus of our study5, we managed to bring the special problems
of the VIPs under the attention of the persons who are in charge of
telebanking at the different banks. Some banks are making account-
certificates in braille or large print (by enlarged photocopy) for their
customers.



























































____________________
5 The results are published in "INFOVISIE MAGAZINE" (Dutch) / "MAGAZINE
 INFOVISION" (French) annual 3, nr. 3.