A practical automated bilateral translation system between printed music 
and Braille.

Hideyuki Sawada, Toshiaki Matsushima, Takebumi Itagaki, Sadamu Ohteru and 
Shuji Hashimoto

1. Introduction

Although music has long been familiar to the blind, it is not always easy
to get braille musical scores. Because braille music production requires
knowledge of music, braille and braille music, mastering braille music is
as difficult as mastering a foreign language. Several attempts at
computerized braille music translation systems have already been
reportedH15. However, in most of them, the translatable symbols in the
score are limited to several fundamental symbols such as notes and rests,
excluding chords. Furthermore, the experiments were mostly done by the
researchers in their own laboratories for only part of the particular
score.

Over the past ten years, we have developed an automated printed-to-braille
music translation system at our laboratoryH25. It has the capability of
converting almost all the symbols in a musical score for piano and their
complex combinations into braille. At the same time, we have been
developing a braille-to-printed music (inverse) translation system, and
construct a bilateral translation system.

Recently, this  bilateral translation system has been redesigned and
simplified for practical use by means of a 16bit-microcomputer. The
redesigned system aims to be used without special equipment in any place by
any person, not just music, braille and computer specialists. Before
rearranging the system and carrying out practical tests, we discussed the
scope of testing in detail in cooperation with Mr. T.Kato (Nippon
Lighthouse Welfare Center for the Blind) and Mr. K.Oka (Dai-Nippon Printing
Co.,LTD.). In order to make a simple application environment, hardware and
software for testing have been extremely restricted as listed in Table 1.
The necessary hardware is a conventional microcomputer with additional
memory of 1-2 Mbytes and a braille-writer, both of which are available in
virtually any place in this country. The necessary software was lent to
users free of charge during the testing period. Fortunately, six public and
one private institutions cooperated in our practical testing task: Nippon
Lighthouse Welfare Center for the Blind, Tokyo Helen Keller Association,
The National Institute of Special Education, National Rehabilitation Center
for the Disabled, University of Tsukuba School for the Blind, Japan Braille
Library, and New Braille System.

2. The Waseda Music Information Processing Sytem

Before explaining the practical system, we will describe the Waseda
integrated music information processing system, PSB-er, which we have
developed in our laboratory for education and research, briefly from the
standpoint of bilateral translation.

Printed and braille musical scores, and musical performance are three major
expressions of musical information used globally as universal languages.
PSB-er is able to input and output any of these three representations.
However, the expression of these three forms is quite different.
Consequently, we contrived a commonly usable data format SMX (Standard
Music eXpression). Furthermore, for the translation between printed and
braille, one more data format, Internal Data Format, was needed between SMX
and braille data which correspond to NABCC (North American Braille Computer
Codes), to make them interchangeable. The system configuration is shown in
Fig.1 by the dotted lines. Since the system is integrated from the
viewpoint of on-line operation, the optical scan type automatic score
reading device is mainly used for score data entryH55. The DMP (Dai-Nippon
Music Processor), which is a commercially available manual device for score
information entry with icon and mouse, was prepared for secondary use.

Once musical data is entered or stored into the system, it can be retrieved
in any of the three music forms. The automatic printed-to-braille music
translation system produces a braille musical score and automatically
embosses it out to the braille-writer. The translation can be seen on the
CRT display. Musical data can be also obtained in the form of musical sound
using a music synthesizer or as a printed score.

One example of a translation is shown in Fig.2-1 and Fig.2-2. Figure 2-1 is
the original score, which consists of two parts, and Figure 2-2 is the
translated result. The chords, slur, crescendo, fingering, and the complex
combination of these symbols are completely translated into braille. Almost
all the symbols in piano musical score are translatable, including notes
and rests from 128th to whole, dots, accidentals, chords, expression marks,
fingering, pedal signs, hand signs, clefs, key signatures, time signatures,
slurs, ties, crescendo, decrescendo, expression words, 8 va. and bars. In
addition to these symbols, the unique signs of braille music, such as the
octave sign and the braille repeat sign, are also translatable.

Braille musical data produced by the printed-to-braille translation system
can be viewed in the form of a printed score with the help of the inverse
translation system.

3. Practical testing system

To handle the first step of a practical system easily, we restricted some
important symbols: notes, rests, dots, accidentals, chords, expression
marks such as staccato and tenuto, clefs, key signatures, time signatures,
bars such as normal bar, double bar and end bar. And necessary hardware and
software to the tests are also limited as shown in Table 1.

The data-flow of the system is shown in Fig.1 by the block lines. To enter
printed music data, two kinds of data are applicable, but the data directly
obtained by the users with the aid of the DMP is mainly used. The SMX data
previously obtained by the automatic music-score reading device is used
only secondarily. Since the DMP, the main part of which is composed of a
microcomputer, was originally developed for general music score printing,
it can input many kinds of scores, and a variety of formats, symbols and
note sizes. In cooperation with Dai-Nippon Printing Co., LTD., the DMP has
had its unnecessary functions removed. It is used exclusively for inputting
and can be used as the data entry device of this system by adding only a
1Mbyte RAM to one commonly used microcomputer with one diskette. The
rearranged DMP becomes quite easy to operate and saves loading time,
although its operation seemed to be, as is mentioned later, still a bit
troublesome for novice users. The data obtained by the DMP after being
converted into SMX are translated into braille data and embossed. With the
aid of a braille-processor, (a braille-writer with exclusive software),
which can be used not only as an input device but also as an editing device
of braille in NABCC on a microcomputer, users can modify the data produced
and add symbols and other items at will.

For the inverse translation system, three kinds of data are available,
though data obtained by the automatic translation system of printed-to-
braille, and that input by the braille-processor are mainly used. As for
the automatic braille recognition system, some different methods are
considered and tested. The braille data written in the same form as the one
obtained by the translation system is analyzed and converted into internal
format data, then into SMX.

Braille music, however, has no note position or graphical coordinate
information, which is important for printed music scores. In the PSB-er, a
printed score is produced directly from internal data format on the CRT,
measure by measure, in which notes and rests are distributed with the same
intervals.

On the other hand, the DMP also has an automatic score-editing command, by
which notes and rests are located in their suitable positions on staves
determined by the DMP rules. For a practical testing system, in which the
DMP could be used as a device for producing scores, a program which
converts the internal data format into SMX was developed because SMX and
DMP data can be converted into each other. By roughly adding coordinates
which represent score information that shows the order to be distributed,
SMX data with temporary coordinates are converted into DMP data. The final
results, after being automatically edited on the DMP, can be printed out as
a printed score. They can also be reproduced as an actual sound using a
music generator or MIDI.

One of the examples of the practical system is shown in Figs.2-1,3-1 and 3-
2. Figure 2-1 shows an original score. Figure 3-1 shows the braille
obtained by the practical testing translation system. Figure 3-2 shows an
inverse translated score of the braille shown in Fig.3-1. The data confirms
that the two processes are indeed the reverse of each other.

4. Practical tests and its evaluation

A "Manual of Printed-to-Braille and Braille-to-Printed music score
translation system for practical use" and a questionnaire have been
prepared for users. A "Manual for the DMP" was also delivered. Before
testing the system, Waseda university students went to the seven
institutions mentioned, explained it directly, and gave demonstrations
lasting for two or three hours. During the test period, we could maintain
close contact with them and follow their progress. The following answers
and evaluations were obtained through the questionnaires.
(1) Translation System
1. Mistranslation         Yes : 4    No : 1    No answer : 2
2. Symbols and items to be added in the future system
   ties,  slurs,  arpeggios,  breath,  grace notes,  fermatas,  stem,
   fingering,  words,  staccato,  title,  tuplets,  in-accord sign,
   repeat etc.
3. Operation of the system
   Easy : 0     Normal : 2     Complicated : 2     No answer: 3
4. Comments from the users
    A score including several voice parts per one part should be added.
    Extra parts still exist which are not directly related to the
    translation. The system must be simplified for novice users.
(2) Editing after Translation
1. Symbols added by the users
   ties,  slurs,  dynamics,  crescendo,  decrescendo,  repeat sign,
   words,  braille repeat sign,  tuplet,  in-accord sign,  tempo etc.
2. Comments from the users
    When modifications are necessary in three parts or more, it may be
     faster in present state to input directly in braille form without
     editing.
(3) Manual for Users
1. Manual description
   Easy to understand : 2         Normal : 2
   Hard to understand : 2         No answer : 1
2. Comments from the users
   Manual is too long.
   Too many technical terms.
   Difficult to understand the order or procedure of the operation.
(4) Total Evaluation
    The system
    can be practically used without any change.           1
    can be practically used with minor modification.      6
    must be largely improved for practical use.          0
    cannot be practically used.                           0
    The reason for the above answers:
    It is difficult to use and takes a lot of time to input music
     scores from the DMP using a mouse.
    Disk handling is complicated.
(5) Opinions and Comments from the Users for the Whole System
    Translation time becomes shorter.
    Once you are accustomed to it, it will be easier to handle.
    A short course for training the system should be given in order to
     spread its use more widely.
    The system will be useful for braille music education.

There were some translation errors found as pointed out in the
questionnaires. One of the reasons is the system did not know what to do
when an error occurred, which caused it to stop or generate further errors.
The problem has been solved by further routine software development.

5. Conclusions

An automated bilateral translation system between printed music and braille
has been constructed for practical use using a microcomputer and other
commercially available devices, in which special knowledge of music or
braille is not required. It takes only seconds for translation and a few
minutes for inverse translation.

The system was evaluated by users as being useful for practical use with
minor modification. Items to be modified are mainly divided into the
following:
1) Troublesome procedure for data entry, especially in printed scores.
2) Increase of number of translatable symbols.

The above are contrary requirements. Indeed, as shown in 4.(2)1. of the
questionnaires, users reported to add during their editing process some
symbols, most of which had been removed from the PSB-er system to handle
the first step of a practical system easily. We think a simple data entry
device is more important for practical use, even though it causes the
decrease of translatable symbols in the system's present state. However,
the convenient printed score data entry device through music performance
will be commercially available in the near futureH65. We are also
developing this system. Moreover, musical computer codes are directly
obtained in printed music score produced under a CTS system without a
special entry device. As a result, we expect data entry will gradually
become easier for not complicated printed music.

On the other hand, in inverse translation, braille data entry is rather
easy compared with that of printed music data. Therefore, our inverse
translation system might be estimated than we expected, although it is used
effectively for checking the results of the printed-to-braille music
translation.

Our goal is for it to be used without special equipment, in any place and
by any person, not just music experts, and braille music and computer
specialists. Although several problems as mentioned above remain unsolved,
a prototype of the practical testing system has been successfully
constructed. We hope the system will be used as translation assistant or as
an education device for braille music.

Acknowledgement

The authors are obliged to Mr.K.Oka, Dai-Nippon Printing Co., Ltd., and
Mr.T.Kato, Nippon Lighthouse Welfare Center for the Blind, for valuable
suggestions and comments. We are also obliged to the National Institute of
Special Education, National  Rehabilitation Center for the Disabled, Japan
Braille Library, Tokyo Helen Keller Association, Nippon Lighthouse Welfare
Center for the Blind, University of Tsukuba School for the Blind, New
Braille System, for their cooperation of the practical tests. In addition,
we are obliged to the Dai-Nippon Printing Co., Ltd., New Braille System and
IO Data for the supply of software and hardware. The authors gratefully
acknowledge all these people for their support and encouragement in the
practical tests.

References

H15 For example, H. Humphreys," A Computerbased System for Production of
Braille Music", Computerized Braille Production, 1983, 243-252.
H25 T. Matsushima, "Automated Printed-Music-to-Braille Translation System",
Journal of Information Processing, Vol.11, No.4, 1988, 249-257.
H35 S. Ohteru et al., "An Integrated Music Information Processing System:
PSB-er", International Computer Music Conference, September, 1988, Koeln.
Proc. 1989 ICMC, 191-198.
H45 S. Ohteru, K. Oka et al., "A Musical Data Expression for Integrated
Music Information System: SMX", 3K-3, Proc. 36th Annual Convention IPS
Japan, March 1988 (Japanese).
H55 S. Ohteru et al., "Automated High Speed Recognition of Printed Music
(WABOT-2 Vision System)", Proc. International Conference on Advanced
Robotics, Tokyo, September, 1985, 477-482.
H65 For example, Music Printer Plus, PC Magazine, March, 1989.